## Slide 1
AGENTIC AI FOR RTL VERIFICATION
Agentic AI for Failure Triage and Root-Cause Hinting in NN Accelerator Verification
An end-to-end AI pipeline for automated RTL verification triage
July 2026
342x speedup
96.5% accuracy
131 tests
255 records
13 fault variants

## Slide 2
INTRODUCTION
The Problem
NN Accelerator Triage | Agentic AI for RTL Verification
02 / 40
• Verification costs 60-70% of total chip development time
• A single chip has millions of simulation failures per tapeout cycle
• Engineers manually read logs, hypothesize root causes, run follow-up tests
• Average 45 minutes per failure cluster for an experienced engineer
• Bottleneck: expert-dependent, slow, error-prone, not scalable

## Slide 3
INTRODUCTION
Why Neural Network Accelerators
NN Accelerator Triage | Agentic AI for RTL Verification
03 / 40
• NN accelerators are the fastest-growing chip category (GPUs, TPUs, NPUs)
• Complex fixed-point arithmetic: quantization, accumulation, memory arbitration
• Unique failure modes: sign extension errors, accumulator overflow, quantization drift
• Verification complexity grows with model size and precision requirements

## Slide 4
INTRODUCTION
Our Solution
NN Accelerator Triage | Agentic AI for RTL Verification
04 / 40
• Build a layered testbench for a small NN accelerator RTL
• Inject fault variants to create a realistic regression database
• Extract features from failures automatically
• Cluster failures by symptom using rule-based + DBSCAN
• Generate natural-language root-cause reports using Claude AI
• Benchmark AI triage speed and accuracy against manual baseline

## Slide 5
INTRODUCTION
Five Core Objectives
NN Accelerator Triage | Agentic AI for RTL Verification
05 / 40
• (i) Verify functional correctness across tensor shapes, quantization, memory behaviors
• (ii) Cluster regression failures automatically
• (iii) Generate natural-language debug summaries and root-cause hints
• (iv) Compare triage time against manual methods
• (v) Package a reproducible failure-analysis benchmark others can run

## Slide 6
INTRODUCTION
Key Results Preview
NN Accelerator Triage | Agentic AI for RTL Verification
06 / 40
• 342x speedup on original benchmark (4 faults, 27 records)
• 293x speedup on expanded benchmark (13 faults, 255 records)
• 96.5% classification accuracy on detectable faults
• 33 latent faults detected (passed simulation but contain RTL bugs)
• 131 tests passing, fully reproducible with Docker
• Open-source benchmark dataset released

## Slide 7
PROJECT ARCHITECTURE
Full Pipeline Overview
NN Accelerator Triage | Agentic AI for RTL Verification
07 / 40
RTL Design
CocoTB Simulation
regression_ db.jsonl
Feature Extractor
Clusterer
Triage Agent
RAG Store
Debug Loop
Benchmark
Dashboard
One append-only log feeds a fully automated clustering + LLM triage pipeline, ending in a self-contained HTML dashboard.

## Slide 8
PROJECT ARCHITECTURE
Technology Stack
NN Accelerator Triage | Agentic AI for RTL Verification
08 / 40
• RTL: SystemVerilog (Verilator 5.x simulator)
• Testbench: CocoTB 2.0.1 (Python-based hardware simulation)
• Reference Models: NumPy (pure Python golden models)
• AI: Claude Sonnet 4.6 via Anthropic API
• Clustering: scikit-learn DBSCAN + rule-based classifier
• RAG: TF-IDF similarity (sklearn)
• Testing: pytest (131 tests)
• Packaging: Docker + docker-compose

## Slide 9
PROJECT ARCHITECTURE
Project Timeline (20 Sessions)
NN Accelerator Triage | Agentic AI for RTL Verification
09 / 40
Session | Phase | Goal | Deliverable
1-4 | Phase 1 (RTL) | Write 4 RTL modules | mac_array.sv, quant_unit.sv, mem_arbiter.sv, control_fsm.sv
5 | Phase 1 | NumPy reference models | mac_ref.py, quant_ref.py (36 tests)
6-7 | Phase 1 | CocoTB testbenches | test_mac_array.py, test_quant_unit.py (51 tests)
8 | Phase 2 | Fault injection + regression DB | 4 fault variants, 27 records, mismatch schema
9 | Phase 2 | Feature extractor | 13 features per record (64 tests)
10 | Phase 2 | Clusterer | DBSCAN + rule-based (79 tests)
11 | Phase 3 | Triage agent | Claude API integration (87 tests)
12 | Phase 3 | RAG store | TF-IDF similarity retrieval (101 tests)
13 | Phase 3 | Multi-turn debug loop | Convergence criteria (106 tests)
14 | Phase 4 | Ground truth + eval metrics | precision/recall/F1 (111 tests)
15 | Phase 4 | Benchmark runner | 342x speedup result (116 tests)
16 | Phase 4 | Dashboard | Static HTML dashboard (120 tests)
17 | Phase 4 | Docker + README | One-command reproduce (120 tests)
18-19 | Sprint | 13 faults + VCD parser + abstract | 96.5% accuracy (131 tests)

## Slide 10
PROJECT ARCHITECTURE
Repository Structure
NN Accelerator Triage | Agentic AI for RTL Verification
10 / 40
• rtl/: SystemVerilog RTL modules + 13 fault variants
• tb/: CocoTB testbench + NumPy reference models
• triage/: Feature extractor, clusterer, triage agent, RAG store, debug loop
• benchmark/: Benchmark runner, evaluator, ground truth labels
• dashboard/: Static HTML dashboard generator
• reports/: Generated outputs (dashboard.html, benchmark JSON, REPORT.md)
• docker/: Dockerfile, run_pipeline.sh, docker-compose.yml
• regression_db.jsonl: 255-record append-only central log
• requirements.txt + pytest.ini: Python dependencies and test config

## Slide 11
RTL DESIGN & TESTBENCH
RTL Module 1: mac_array.sv
NN Accelerator Triage | Agentic AI for RTL Verification
11 / 40
• Parameterized NxN systolic-style MAC array (default N=4)
• DATA_TYPE: INT8 (8-bit in, 32-bit acc), INT16 (16-bit in, 48-bit acc), FP16 stub
• FSM: IDLE → COMPUTE (N cycles) → DONE
• AXI-style valid/ready handshake on input and output
• Synchronous active-low reset
• Lint-clean: zero Verilator warnings

## Slide 12
RTL DESIGN & TESTBENCH
RTL Module 2: quant_unit.sv
NN Accelerator Triage | Agentic AI for RTL Verification
12 / 40
• Per-channel INT8 asymmetric quantization
• Formula: q[i][j] = clamp(((acc[i][j] * scale[i]) >>> shift[i]) + zero_pt[i], -128, 127)
• Channel axis = output row; per-channel scale (16-bit), shift (5-bit), zero_pt (INT8)
• Single-cycle latency (combinational quantization path)
• PROD_W = ACC_W + SCALE_W + 1 = 49-bit intermediate precision

## Slide 13
RTL DESIGN & TESTBENCH
RTL Modules 3 and 4
NN Accelerator Triage | Agentic AI for RTL Verification
13 / 40
mem_arbiter.sv
• Shared SRAM arbiter for weight and activation memory
• Round-robin arbitration, bank-conflict detection
• 1-cycle stall penalty on conflict
control_fsm.sv
• Top-level sequencer instantiating all 3 modules
• FSM: IDLE → LOAD → COMPUTE → QUANTIZE → STORE → DONE
• Start/done pulse handshake

## Slide 14
RTL DESIGN & TESTBENCH
CocoTB Testbench
NN Accelerator Triage | Agentic AI for RTL Verification
14 / 40
• CocoTB 2.0.1 with Verilator 5.x backend
• SV wrapper modules flatten unpacked 2D ports to packed flat buses (VPI limitation)
• Handshake protocol: valid/ready, ReadOnly() phase discipline
• 21 mac_array tests × 3 configs = 63 test runs
• 30 quant_unit tests × 3 configs = 90 test runs
• All expected values from NumPy reference models — no hardcoded results

## Slide 15
RTL DESIGN & TESTBENCH
NumPy Reference Models
NN Accelerator Triage | Agentic AI for RTL Verification
15 / 40
mac_ref.py
• Pure NumPy NxN matrix multiply
• INT8 → int32 output, INT16 → int64 (48-bit wrapped), FP16 → zeros
• Matches mac_array.sv exactly: sign-extension, accumulator wrap
quant_ref.py
• Per-channel asymmetric INT8 quantization
• Arithmetic right-shift via Python int (arbitrary precision, no int64 overflow)
• Matches quant_unit.sv formula exactly

## Slide 16
RTL DESIGN & TESTBENCH
Test Suite Growth
NN Accelerator Triage | Agentic AI for RTL Verification
16 / 40
After Session 5
36 tests
After Session 7 (CocoTB added)
51 tests
After Session 8 (TestGenerator added)
56 tests
After Session 9 (feature extractor added)
64 tests
After Session 10 (clusterer added)
79 tests
After Session 13 (full triage pipeline)
106 tests
After Session 17 (benchmark + dashboard)
120 tests
Final (Session 18-19)
131 tests
All sessions: 0 failures

## Slide 17
FAULT INJECTION
Fault Injection Methodology
NN Accelerator Triage | Agentic AI for RTL Verification
17 / 40
• 13 fault variants across mac_array.sv and quant_unit.sv
• Each fault = exactly one targeted string substitution in the RTL
• scripts/generate_faults.py verifies exactly one diff hunk per file
• Software fault models in Python mirror each RTL change for DB population
• Two types: detectable faults (cause simulation failures) and latent faults (pass simulation)

## Slide 18
FAULT INJECTION
mac_array Fault Variants
NN Accelerator Triage | Agentic AI for RTL Verification
18 / 40
Variant | Change | Effect | Detectable?
fault_acc_overflow | ACC_W 32→16 | Wraps at ±32,767 | Yes
fault_wrong_sign | A_reg signed→unsigned | Zero-extends A | Yes
fault_off_by_one | loop exit N-1→N-2 | Misses last product | Yes
fault_reset | !rst_n→rst_n | Never resets | Yes
fault_acc_w24 | ACC_W 32→24 | Latent for N=4 INT8 | No
fault_acc_w20 | ACC_W 32→20 | Latent for N=4 INT8 | No
fault_loop_over | i<N → i<=N | OOB write row 0 | Yes
fault_subtract | acc + → acc - | Negated products | Yes
fault_b_unsigned | B_reg signed→unsigned | Zero-extends B | Yes

## Slide 19
FAULT INJECTION
quant_unit Fault Variants
NN Accelerator Triage | Agentic AI for RTL Verification
19 / 40
Variant | Change | Effect | Detectable?
fault_quant_reset | !rst_n→rst_n | Never resets | Yes
fault_quant_shift_fixed | shift[i]→1 | Wrong shift amount | Partially
fault_quant_no_clamp | clamp removed | Values wrap | Partially
fault_quant_wrong_sign_zp | zero_pt signed→unsigned | Wrong bias | Partially
(golden: no fault, all pass)

## Slide 20
FAULT INJECTION
The Latent Fault Finding
NN Accelerator Triage | Agentic AI for RTL Verification
20 / 40
• 33 out of 255 records PASS simulation despite containing injected RTL bugs
• Breakdown: fault_acc_w24 (12), fault_acc_w20 (12), 3 quant latent records (9)
• Why latent: max possible sum for N=4 INT8 is 64,516 — fits in 20 and 24 bits
• Standard regression: engineer sees green checkmark, assumes RTL is correct
• Our system: latent_fault cluster flags these as suspicious
• Fix: increase N, use larger inputs, or apply formal verification
• This is a REAL industry problem — latent bugs cause post-silicon failures

## Slide 21
FAULT INJECTION
Regression Database Schema
NN Accelerator Triage | Agentic AI for RTL Verification
21 / 40
run_id: UUID string
timestamp: ISO-8601 UTC
dut: mac_array | quant_unit
variant: golden | fault_*
config: {n, data_type, acc_w}
test_name: short description with seed
status: pass | fail | error
mismatch_details: null (pass) or {total_elements,
: mismatch_count, max_abs_error, first_mismatch}
255 records
total regression database size
87 golden passes
golden RTL, zero mismatches
33 latent passes
fault variants that still pass
135 detectable failures
fault variants that fail

## Slide 22
AI TRIAGE PIPELINE
Feature Extractor
NN Accelerator Triage | Agentic AI for RTL Verification
22 / 40
• Identity: run_id, dut, variant, test_name, status
• Config: config_n, config_data_type, config_acc_w
• Numeric: mismatch_rate (0.0-1.0), max_abs_error
• Bucketed: error_magnitude_bucket (none/small/medium/large)
• Symptom flags: has_reset_symptom, has_overflow_symptom
• Waveform: first_divergence_cycle, total_cycles (from VCD parser)
13 features extracted per record

## Slide 23
AI TRIAGE PIPELINE
Rule-Based Clusterer
NN Accelerator Triage | Agentic AI for RTL Verification
23 / 40
• 1. has_reset_symptom=True → reset_fault
• 2. has_overflow_symptom=True → overflow_fault
• 3. bucket=large, no overflow/reset → sign_error OR arithmetic_error
• 4. bucket=medium, rate≥0.999 → off_by_one
• 5. quant faults by error range → shift_error / saturation_error / zero_point_error
• 6. status=pass, variant≠golden → latent_fault
• 7. status=pass, variant=golden → clean_pass
• 8. else → uncategorized
Plus DBSCAN on 5-element normalized feature vector for outlier detection

## Slide 24
AI TRIAGE PIPELINE
Triage Agent
NN Accelerator Triage | Agentic AI for RTL Verification
24 / 40
• Groups clustered records by cluster_label
• Skips clean_pass (no API call needed)
• For each failure cluster: builds rich prompt with test names, mismatch rates, error ranges, symptom flags
• Calls claude-sonnet-4-6 (max_tokens=1024 for large clusters)
• Parses JSON response: likely_cause, confidence, recommended_debug_steps, affected_configs
• affected_configs built deterministically from records (not from Claude) to prevent hallucination
• Falls back gracefully on API error or malformed JSON

## Slide 25
AI TRIAGE PIPELINE
RAG Store
NN Accelerator Triage | Agentic AI for RTL Verification
25 / 40
• Stores historical triage reports for retrieval
• Each record converted to token string: label_overflow_fault bucket_large dut_mac_array n_4 rate_very_high overflow_symptom
• TF-IDF vectorizer fits on all stored tokens
• Cosine similarity query returns top-k most similar past failures
• Each result includes: similarity score + matched_fields list (explainable)
• Lazy index rebuild: only refit when new entries added
• Save/load to JSON for persistence across sessions

## Slide 26
AI TRIAGE PIPELINE
Multi-Turn Debug Loop
NN Accelerator Triage | Agentic AI for RTL Verification
26 / 40
• Wraps triage agent in iterative conversation
• Turn 1: initial hypothesis from cluster summary
• If confidence < high: generates programmatic follow-up question
‣ overflow symptom not mentioned → ask about accumulator width
‣ reset symptom not mentioned → ask about reset polarity
‣ otherwise → ask for alternative hypothesis
• Turn N: refined hypothesis with updated confidence
• Converges when confidence = high OR max_turns reached (default 3)
• Returns: final report + full conversation history + converged flag

## Slide 27
AI TRIAGE PIPELINE
Example Triage Report: overflow_fault
NN Accelerator Triage | Agentic AI for RTL Verification
27 / 40
Cluster: overflow_fault (3 records)
CONFIDENCE: HIGH
Likely cause: Accumulator declared as 16-bit signed instead of required 32-bit width. Large partial sums wrap at ±32,767, producing the characteristic 65,536 error magnitude.
Recommended debug steps
1. Check ACC_W parameter in mac_array.sv — should be 32 for INT8
2. Add directed test with all-127 inputs to force accumulator overflow
3. Probe accumulator MSB in waveform at end of COMPUTE state
Affected configs: mac_array/N=4/fault_acc_overflow

## Slide 28
AI TRIAGE PIPELINE
Example Triage Report: latent_fault
NN Accelerator Triage | Agentic AI for RTL Verification
28 / 40
Cluster: latent_fault (33 records)
CONFIDENCE: HIGH
Likely cause: These are pass results from fault variants where the injected bug is mathematically undetectable with current test vectors. The accumulator narrowed to 20-24 bits cannot overflow with 8-bit inputs and N=4 accumulation steps (max sum = 64,516 < 2^20).
Recommended debug steps
1. Increase N or use larger input magnitudes to exercise the fault
2. Add directed tests targeting accumulator boundary values
3. Consider formal verification for latent coverage gaps
Affected configs: mac_array/N=4/fault_acc_w20, mac_array/N=4/fault_acc_w24

## Slide 29
AI TRIAGE PIPELINE
VCD Waveform Parser
NN Accelerator Triage | Agentic AI for RTL Verification
29 / 40
• Verilator generates dump.vcd in sim_build_*/ directories
• triage/vcd_parser.py parses VCD using Python stdlib only
• Extracts: first_divergence_cycle, total_cycles, diverging_signals
• first_divergence_cycle: clock cycle when out_valid first goes high
• Reset faults diverge at cycle 0-2; accumulator faults diverge later
• Adds temporal context to feature vectors for clustering
• Handles missing/empty VCD gracefully (returns None)

## Slide 30
BENCHMARK & EVALUATION
Evaluation Methodology
NN Accelerator Triage | Agentic AI for RTL Verification
30 / 40
• Ground truth: benchmark/ground_truth.json maps each variant to canonical label
• 9 ground truth labels: no_fault, accumulator_overflow, sign_extension_error, loop_boundary_error, arithmetic_error, reset_polarity_error, shift_error, saturation_error, zero_point_error
• Metrics: precision, recall, F1 per label + overall accuracy
• Implemented from scratch (no sklearn) using confusion matrix
• Manual baseline: 45 minutes per failure cluster (industry estimate)
• Speedup = manual_baseline_seconds / total_ai_time

## Slide 31
BENCHMARK & EVALUATION
Main Results (Expanded Benchmark)
NN Accelerator Triage | Agentic AI for RTL Verification
31 / 40
Metric | LLM-Augmented | Rule-Based Only
Overall accuracy | 96.5% (246/255) | 96.5% (246/255)
Mean confidence | 0.600 | 0.000
AI pipeline time | 46 s | 0.1 s
Manual baseline | 225 min | 225 min
Speedup vs manual | 293x | 63,000x
Latent faults detected | 33/255 | 33/255
Failure clusters | 9 | 9
Test suite | 131 tests, 0 failures | —

## Slide 32
BENCHMARK & EVALUATION
Per-Label Precision / Recall / F1
NN Accelerator Triage | Agentic AI for RTL Verification
32 / 40
Label | Precision | Recall | F1 | Support
accumulator_overflow | 0.812 | 1.000 | 0.897 | 39
arithmetic_error | 1.000 | 1.000 | 1.000 | 12
loop_boundary_error | 1.000 | 1.000 | 1.000 | 27
no_fault | 1.000 | 1.000 | 1.000 | 87
reset_polarity_error | 1.000 | 1.000 | 1.000 | 27
saturation_error | 1.000 | 0.750 | 0.857 | 12
shift_error | 1.000 | 0.750 | 0.857 | 12
sign_extension_error | 1.000 | 1.000 | 1.000 | 27
zero_point_error | 1.000 | 0.750 | 0.857 | 12
Overall | 0.965 |  |  | 255

## Slide 33
BENCHMARK & EVALUATION
Why Accuracy Is Equal for Rule-Based and LLM
NN Accelerator Triage | Agentic AI for RTL Verification
33 / 40
• Rules handle KNOWN fault categories — already near-optimal at 96.5%
• LLM cannot improve classification accuracy on pre-defined categories
• LLM VALUE is elsewhere:
‣ Natural language explanation of root cause
‣ Actionable debug steps (which file, which line, which test)
‣ Confidence scoring (flags ambiguous cases)
‣ Novel fault handling (rules return uncategorized; LLM still reasons)
• This is an honest and important finding: LLM as explainer, not classifier

## Slide 34
BENCHMARK & EVALUATION
Pipeline Stage Timing
NN Accelerator Triage | Agentic AI for RTL Verification
34 / 40
Load + parse <0.1%
2.5 ms
Feature extraction <0.1%
0.6 ms
Clustering (DBSCAN) 0.2%
87 ms
Claude API triage 99.8%
46.0 s
Evaluation <0.1%
0.3 ms
Total ≈ 46 s with LLM. Without LLM: total = 90 ms (63,000x speedup)

## Slide 35
DISCUSSION
The Latent Fault Problem
NN Accelerator Triage | Agentic AI for RTL Verification
35 / 40
• 33 records PASS simulation = standard regression marks them GREEN
• Engineer sees no failures, assumes RTL is correct
• Reality: RTL contains an injected bug that will manifest with different inputs
• Our system correctly labels them latent_fault and flags for investigation
• Root cause: test vectors don't stress the fault condition
• Industry relevance: latent bugs discovered post-silicon cost millions to fix
• Our contribution: systematic detection of simulation-passing fault variants

## Slide 36
DISCUSSION
Honest Limitations
NN Accelerator Triage | Agentic AI for RTL Verification
36 / 40
• Toy RTL: 4x4 MAC array, not real silicon (NVDLA, Gemmini)
• Estimated baseline: 45 min/cluster is an industry estimate, not measured
• No timing faults: setup/hold violations, pipeline hazards not covered
• No memory faults: wrong addressing, DMA errors not covered
• Small benchmark: 255 records vs thousands in real tapeouts
• Circular accuracy: rules designed for exactly these fault types

## Slide 37
DISCUSSION
Future Work
NN Accelerator Triage | Agentic AI for RTL Verification
37 / 40
Short Term (1-3 mo)
• Port to real open-source accelerator: Gemmini or NVDLA
• Systematic mutation testing: 100+ auto-generated faults
• User study: time real verification engineers (Intel connection)
• Measured manual baseline: replace estimate with real data
Medium Term (3-6 mo)
• Timing fault detection via waveform analysis
• Memory fault categories
• Multi-design generalization test
• Model ablation: Claude vs GPT-4 vs Llama
Long Term (6-12 mo)
• Paper submission: ASP-DAC 2027 or DATE 2027
• VS Code / EDA plugin for inline triage hints
• Proprietary failure database from industry partnerships

## Slide 38
CONCLUSION
Summary of Contributions
NN Accelerator Triage | Agentic AI for RTL Verification
38 / 40
• 1. Complete end-to-end agentic AI pipeline for RTL verification triage
• 2. Open-source benchmark dataset: 255 records, 13 fault variants, 9 categories
• 3. Latent fault detection: 33 simulation-passing bugs correctly flagged
• 4. Quantitative evaluation: 96.5% accuracy, 293x speedup
• 5. Honest ablation: rule-based vs LLM — equal accuracy, LLM adds explanation
• 6. Fully reproducible: Docker, pytest, one-command pipeline
• 7. 131 passing tests, zero failures across all sessions

## Slide 39
CONCLUSION
Open Source Release
NN Accelerator Triage | Agentic AI for RTL Verification
39 / 40
• Full RTL source: mac_array, quant_unit, mem_arbiter, control_fsm
• Fault variants: 13, with documented injection methodology
• Regression database: 255-record dataset with JSON schema
• Triage pipeline: feature extractor, clusterer, triage agent, RAG, debug loop
• Benchmark tooling: runner and evaluator
• Dashboard: interactive HTML report
• Reproducibility: Docker for one-command reproduce
• Test suite: 131 pytest tests
GitHub: https://github.com/Sumedh350/nn-accel-triage

## Slide 40
Questions?
342x speedup
96.5% accuracy
131 tests
13 fault variants
255 records
GitHub: https://github.com/Sumedh350/nn-accel-triage
40 / 40